## Slide 1: Introduction to Labs
Wenchao Cao, Teaching Assistant
Department of EECS
University of Tennessee

## Slide 2: Outline
Software
  Xilinx ISE Design Suite 13.2 WebPACK
  Digilent Adept 2.0
Hardware
  Digilent BASYS Board (Xilinx Spartan 3E FPGA)
  Digilent BASYS 2 Board (Xilinx Spartan 3E FPGA)
Example
Demo
Lab Report Requirements

## Slide 3: Outline
Software
  Xilinx ISE Design Suite 13.2 WebPACK
  Digilent Adept 2.0
Hardware
  Digilent BASYS Board (Xilinx Spartan 3E FPGA)
  Digilent BASYS 2 Board (Xilinx Spartan 3E FPGA)
Example
Demo
Lab Report Requirements

## Slide 4: Xilinx ISE Design Suite 13.2 WebPACK
Logic design software including GUI, schematics editor and files for logic symbols, VHDL compiler, “PlanAhead” package to assign I/O pins, utilities to create to a *.bit file to send to the BASYS or BASYS2 board to program the Xilinx Spartan3e FPGA on the board, and TestBench simulator.
We’re using release 13.2, not a later release.
Free
Download link: http://www.xilinx.com/support/download/index.html/content/xilinx/en/downloadNav/design-tools/v13_2.html
Select: Full installer for windows
Need registration

## Slide 5: Digilent Adept 2.0
The software interface to the board that downloads a completed *.bit file via USB connector.
Free
Download link: http://www.digilentinc.com/Products/Detail.cfm?Prod=ADEPT2
Select: Adept 2.13.1 System, 32/64-bit Windows

## Slide 6: Outline
Software
  Xilinx ISE Design Suite 13.2 WebPACK
  Digilent Adept 2.0
Hardware
  Digilent BASYS Board (Xilinx Spartan 3E FPGA)
  Digilent BASYS 2 Board (Xilinx Spartan 3E FPGA)
Example
Demo
Lab Report Requirements

## Slide 7: Digilent BASYS Board (Xilinx Spartan 3E FPGA)
Old version, not preferred.
Description: http://www.digilentinc.com/Products/Detail.cfm?Prod=BASYS
Download “BASYS reference manual” and “BASYS schematic” for references.
I/O pins
Family: Spartan 3E
Device: XC3S100E
Package: TQ144

## Slide 8: Digilent BASYS Board (Xilinx Spartan 3E FPGA)
Please read “BASYS reference manual” (Page 1 to Page 5) very carefully!
Basys programming circuit locations
Select
JTAG
Basys oscillator circuits
Select
The required input clock frequency

## Slide 9: Digilent BASYS 2 Board (Xilinx Spartan 3E FPGA)
New version, preferred.
Description: http://www.digilentinc.com/Products/Detail.cfm?Prod=BASYS2
Download “BASYS 2 reference manual” and “BASYS 2 schematic” for references.
I/O pins
Family: Spartan 3E
Device: XC3S100E
Package: CP132

## Slide 10: Digilent BASYS 2 Board (Xilinx Spartan 3E FPGA)
Please read “BASYS 2 reference manual” (Page 1 to Page 5) very carefully!
Basys 2 programming circuit locations
Select
PC
Basys 2 oscillator circuits
Can only select
50 MHz as the input clock frequency

## Slide 11: Outline
Software
  Xilinx ISE Design Suite 13.2 WebPACK
  Digilent Adept 2.0
Hardware
  Digilent BASYS Board (Xilinx Spartan 3E FPGA)
  Digilent BASYS 2 Board (Xilinx Spartan 3E FPGA)
Example
Demo
Lab Report Requirements

## Slide 12: Example
Work Flow
The figure shows the software tools in a logic design project from schematic to VHDL code to *.bit file for download to BASYS or BASYS2 board.

## Slide 13: Xilinx ISE Design Suite 13.2
Double Click

## Slide 14: Create A New Project

## Slide 15: Project Settings
Choose TQ144 if you are using a BASYS board

## Slide 16: Create New Source Files

## Slide 17: Draw the Schematics
Add wire
Add I/O marker
Add symbol
AND: AND2
OR: OR2
NOT: INV
XOR: XOR2
Quick search of the symbols

## Slide 18: Draw the Schematics
Rename the Ports by right-clicking on them

## Slide 19: Pin Placement & Assignment
Find “Design”
Select the file
Expand the Folder here
Assign pins here

## Slide 20: PlanAhead 13.2

## Slide 21: PlanAhead 13.2

## Slide 22: PlanAhead 13.2
Expand the Folder here
Save your work and exit

## Slide 23: Generate “*.bit file”

## Slide 24: Download the program

## Slide 25: Download the program

## Slide 26: Program the Board

## Slide 27: Results
ABCD = 0000 ABCD = 0001

## Slide 28: Results
ABCD = 0011 ABCD = 0111

## Slide 29: Results
ABCD = 1001 ABCD = 1101

## Slide 30: Results
ABCD = 1100 ABCD = 1111

## Slide 31: Outline
Software
  Xilinx ISE Design Suite 13.2 WebPACK
  Digilent Adept 2.0
Hardware
  Digilent BASYS Board (Xilinx Spartan 3E FPGA)
  Digilent BASYS 2 Board (Xilinx Spartan 3E FPGA)
Example
Demo
Lab Report Requirements

## Slide 32: Demo
Demo
X=AB
Y=A+B

## Slide 33: Outline
Software
  Xilinx ISE Design Suite 13.2 WebPACK
  Digilent Adept 2.0
Hardware
  Digilent BASYS Board (Xilinx Spartan 3E FPGA)
  Digilent BASYS 2 Board (Xilinx Spartan 3E FPGA)
Example
Demo
Lab Report Requirements

## Slide 34: Lab Report Requirements
Completing a lab means demo-ing your work to a GTA and turning in a short written report at the same time.
You are free to work on labs on your own schedule, but each lab must be demo-ed to a GTA sometime during the open lab hours in the week stated on the lab handout.
Return the boards when demo-ing the final lab.

## Slide 35: Lab Report Requirements
Each report must be in this format:
an introductory page with your name and signature, the lab number, a very short description of the goals or objectives of the lab, and a place for the GTA to date and sign off your work;
summaries of your work on each major part of the lab—be sure to tell how you solved any problems you encountered and to refer if necessary to the appendix for schematics, VHDL code, etc;
a concluding statement, short and explicit, of what you learned in the lab and what skill(s) you acquired or improved;
an appendix containing all additional documentation such as
  any schematics,
  any VHDL code,
  any timing diagrams (including simulations),
  all clearly labeled and identified.
Make your reports short and to-the-point. Conciseness and accuracy are your objectives in your reports, not wordiness.

## Slide 36: Beyond the Labs
If you are interested in electronics design,
what else can you do with the BASYS or BASYS 2 board?
Please refer to the “BASYS (2) reference manual”
Be safe! Do not injure yourself or damage the board!
LED Clock
* Pictures are from google.com

## Slide 37: Beyond the Labs
Mini Computer
* Pictures are from google.com
VGA port
PS/2 port
Expansion connectors
* Need to buy the expansion boards from Digilent inc